## Slide 1: HP ProLiant ML150 G5 Server
1. What is new The ML150 G5 server is an Intel-based, 2P, 5U form factor, tower server with up to two Intel Xeon 5400 sequence quad-core processors or 5200 sequence dual-core processors. On 11 February 2008, HP will announce the ProLiant ML150 G5 server as follows: Processor refresh — Up to two (2) Intel Xeon 5400 sequence quad-core processors running at up to 2.83GHz with up to 12MB Level 2 Cache. 2. At-a-glance Available processors — Intel Xeon 5400 sequence quad-core or 5200 sequence dual-core processors. Model E5205 1.86GHz – 6MB dual-core Model E5405 2.00GHz – 12MB quad-core Model E5410 2.33GHz – 12MB quad-core Model E5420 2.50GHz – 12MB quad-core Model E5430 2.66GHz – 12MB quad-core Model E5440 2.83GHz – 12MB quad-core Processor capacity — 2P Form factor — 5U, tower (rack models via optional rack mounting kit) Memory type, protection, and capacity — PC2-5300 DDR2-667,Registered Buffered, 16GB maximum memory I/O — Six expansion slots: two (2) PCI-Express x8, three (3) PCI-Express x4(x8 connector) and one (1) PCI (32-bit/33MHz). One slot designated for optional HP ProLiant Lights-Out 100c remote management card. Storage type — Hot plug or non-hot plug SATA/SAS, up to total 8 Drives with 2nd HDD Option Kit. Storage controller — HP embedded SATA RAID controller, HP SAS SC40Ge PCI Express to 4-Port SATA/SAS HBA controller (SAS model), HP Smart Array E200/128 BBWC SATA/SAS controller (performance model) | Remote management — Optional HP ProLiant Lights-Out 100c Remote Management Card High availability — 750W redundant power supply via optional RPS kit (ready by March Launch) Warranty — 1-1-1 3. Customer opportunities Look for customers with the following business challenges: Remotely manage the server. Why? With the optional Lights-Out 100 card the customer can remotely control the system console and power as well as view the system environmental health and system event log. Also they will have the ability update software and firmware as well as to remotely control attached USB storage. Additionally you can remotely administrate your OS and remotely control the system console. Currently customers would need to walk or drive to the site if something goes wrong with the server. Customer benefits: Remote management capabilities. Small and medium businesses running light applications. Why? ML150 G5 is ideal server for these requirements. Combined with HP Services it can bring the customer the benefit of a faster, simpler deployment with true server functionality. This will yield increased employee productivity, reduced cost of business, and operational efficiency. It can provide basic file/print, database server functionality at an appropriate price point. Customer benefits: ML150 G5 is flexible in deployment. | Cost-conscious, sophisticated small and medium businesses. Why? Affordable dual processor server with essential management, redundancy, and enough power to handle complex business requirements. Customer benefits: Affordable performance-based server, and new technologies provide a competitive edge. Customers who want expandability for future growth. Why? With room for two Intel Xeon processors, six I/O slots, six memory slots, and eight hard drives, the ML150 G5 is optimized for expansion. There is also a rack convertible option kit to meet customer needs in terms of server consolidation. Customer benefits: Many expansion options provide the customer the ability to expand as the business grows. 4. Qualifying the customer Green light deals (must win) The customer: Needs expandability for future growth Needs remote management capabilities Cost conscious SMB looking for an affordable dual processor server Yellow light deals (more qualification) The customer: Size of business may grow beyond 100 employees Red light deals (walk away) The customer: Has dual-core servers and does not feel their business or infrastructure is adversely impacted by their current computing power. 5. Further information/resources For QuickSpecs, white papers, and technical documentation, go to ML150 G5 on HP.com http://www.hp.com/servers/proliantml150
© 2007 Hewlett-Packard Development Company, L.P.
The information contained herein is subject to change without notice.
Quick reference card: HP and channel partner use only

## Slide 2: HP ProLiant ML150 G5 Server
© 2007 Hewlett-Packard Development Company, L.P.
The information contained herein is subject to change without notice.
 | HP ProLiant DL150 G5 | Dell PowerEdge SC1430
Form factor | Tower, 5U | Tower (not rackable)
Processor options | Intel Xeon 5400 sequence (1.8, 2.0, 2.3, 2.5, and 2.83GHz); Intel Xeon 5200 sequence (1.86GHz) | Intel Xeon 5300 sequence quad-core (1.6, 2.0, 2.33, 1.86GHz) Intel Xeon 5100 sequence dual-core (2.0, 1.6GHz)
Max processor cores | 8 (5400 sequence), 4 (5200 sequence) | 8 (5300 sequence quad-core), 4 (5100 sequence dual-core)
Cache | 12MB Level 2 (5400 sequence) 6MB Level 2 (5200 sequence) | 8MB (5300 sequence quad-core), 4MB (5100 sequence dual-core)
Memory min/max | 1GB /16GB | 1GB/8GB
Memory type | Registered buffered DDR2-667 | FBD SDRAM
Disk type | SATA, SAS | SATA, SAS
Disk max internal | 6.0TB SATA, 2.4TB SAS | 4.0TB SATA, 1.2TB SAS
RAID support | HP embedded SATA RAID controller (RAID 0,1) Optional: HP Smart Array E200/128 BBWC SATA/SAS controller (RAID 0,1,5) | Optional: SAS 5iR (when using 2 or less SAS or SATA hard drives and running RAID0 or RAID1 configurations), PERC 5i (only needed when running RAID5 configuration)
I/O technology | PCI-Express, PCI-X | PCI-Express, PCI-X
I/O slot types | Six expansion slots: two (2) PCI-Express x8, three (3) PCI-Express x4(x8 connector) and one (1) PCI (32-bit/33MHz). One slot designated for optional HP ProLiant Lights-Out 100c remote | 5 total I/O slots: 2 PCI Express slots (x4 with x8 connectors), 2 64-bit/100MHz PCI-X slots 3.3V, 1 32-bit/33MHz PCI slot 5V, one full height, full length slot; remaining slots are full height, half length
High availability (hot swap, redundant power supply or fans) | 750W redundant power supply via optional RPS kit (Availability: March 2008) | none
Regional contacts | WW — PJ Lu, pj.lu@hp.com US — Andy Bauman, bauman@hp.com Latin America — Carlos Cuina, carlos.cuina@hp.com EMEA — Yan-Fei Yang, Yan-fei.yang@hp.com AP — Naren Nuggehalli, naren@hp.com Japan — Ikazu Okano, iekazu.okano@hp.com | 
Quick reference card: HP and channel partner use only